## Slide 1: FPGA Acceleration for 3D Low-Dose CT
Ming Jiang
Peking University
ming-Jiang@pku.edu.cn
MS 1 : Applied Mathematics in Tomography
Conference on Modern Challenges in Imaging
2019.08.08
Presentation based on materials/comments from Jason Cong, Yong Cui, William Hsu, Alfred Louis, Xiuhong Li, Yun Liang, Guojie Luo, Peter Maass, Thomas Page, Linjun Qiao, Frank Natterer, Thomas Schuster, Wentai Zhang.

## Slide 2: Outline
Background & Motivation
  Energy-efficient computing with FPGA
Asynchronous parallel iterative algorithms
  Communication model
FPGA implementation
  Techniques for implementation
Summary

## Slide 3: Mumford-Shah functional as a regularization for image reconstruction
Avoid computing derivatives cross edges
Simultaneous reconstruction of image and its segmentation
NP-hard when A is not the identity
Geman and Geman [1984]
Mumford and Shah [1989]
Ambrosio [1989]
De Giorgi, Carriero, and Leaci [1989]
Vese, Chan [2000]
Chan, Esedoglu and Nikolova [2004]
Cai, Chan, Zeng [2013]
Chan, Yang, Zeng [2014]
Rondi and Santosa [2001]
Rondi [2007]
Alexeev, and Ward [2010]
Fornasier, March, Solombrino [2011]
Scherzer [2011, 2014]
Ramlau, Ring [2010]
Klann, Ramlau [2013]
………
Jiang, Maass, Page [2014]
Storath, Weinmann; Frikel, Unser [2015]
Hohm, Storath, Weinmann [2015]
Carriero, Leaci, Tomarelli [2015]
An incomplete list…..

## Slide 4
https://en.wikipedia.org/wiki/Transistor_count
Dark silicon

## Slide 5: Customization and Specialization
Based on Fred Pollack (Intel) and Michael Taylor (UCSD)
Adapt the architecture to application domain
i386
i486
Pentium®
Pentium Pro®
nuclear reactor
Pentium II®
Pentium III®
Pentium® 4
hot plate
rocket nozzle
sun’s surface
Parallelization
Customization
1.5µ
1.0µ
0.7µ
0.5µ
0.35µ
0.25µ
0.18µ
0.13µ
0.10µ
0.07µ
1
10
100
1000
Watts/cm2
Power consumption doubled every 4 years
Curtesy of Prof. Jason Cong
Notes: Muhuan: figure from Michael Taylor, UCSD; data is from Intel

## Slide 6: Energy-efficient computing with FPGA
FPGA is another hardware accelerating approach
  Multi-core-CPU clusters, GPU and DSP,.
FPGA (field-programmable gate array)
  function is defined by a user's program
  reconfigurable for computing
  Limited onboard memory vs others
Xilinx Virtex-7 board VC707 at 100MHz
  485K logic gates, 4.5MB onboard memory
  Transistor count: 6,800,000,000
  4.5W (~consumer LED lamp)
How to make the best use of it?
https://en.wikipedia.org/wiki/LED_lamp

## Slide 7: Logical circuits of an 8-bit Adder
Gate-Level Diagram of an 8-bit Kogge-Stone Parallel Prefix Adder
http://venividiwiki.ee.virginia.edu/.......

## Slide 8: FPGA Implementation of Mumford-Shah Imaging Algorithm
XCT Reconstruction with Mumford-Shah: 200K LUT (logic look-up tables)

## Slide 9: High-level Synthesis C->FPGA
Energy-efficient accelerator-rich architecture
Optimization under the performance, power, and cost constraints
Extensive use of accelerators (algorithmic blocks)
Limited onboard memory with full control including precision
  Extendable
VivadoHLS of Xilinx
  https://www.xilinx.com/products/design-tools/vivado.html
How to design algorithms for FPGA
  to enable the advantages of FPGA
Cong et al, High-Level Synthesis for FPGAs: From Prototyping to Deployment, 2011.

## Slide 10: Outline
Background & Motivation
  Energy-efficient computing with FPGA
Asynchronous parallel iterative algorithms
  Communication model
FPGA implementation
  Techniques for implementation
Summary

## Slide 11: Iterative methods
Many algorithms have the structure
,
Component form
It can be parallelized by letting each one of processors update a component by ,
  at each stage, the -th processor
    has the value of all components of on which depends,
    computes the new value ,
    communicates it to other processors in order to start the next iteration.
Bertsekas and Tsitsiklis, Parallel and distributed computation : numerical methods. 1989.

## Slide 12: Block iterative methods
A coarse-grained parallelization of iterative methods with processors.
Each iteration
, ,
Each is updated by one of the processors.
Reasons
  there may be too few processors available.
  block-parallelization reduces the communication expense.
Bertsekas and Tsitsiklis, Parallel and distributed computation : numerical methods. 1989.

## Slide 13: Jacobi and Gauss-Seidel Iterations
Jacobi-type iteration
all components, simultaneously, updated and made available for next iteration
Gauss-Seidel Iteration
components are updated, one at a time, using the most recently computed values of other components
updated in a cyclic order from to (or for block iterative methods).
One update of all components is a sweep.
Bertsekas and Tsitsiklis, Parallel and distributed computation : numerical methods. 1989.

## Slide 14: Gauss-Seidel Iteration
They incorporate the newest available information.
Hence, they sometimes converge faster than the corresponding Jacobi-type algorithms.
Gauss-Seidel algorithms can have different updating orders for .
In addition to the cyclic order, there are other orders.
Bertsekas and Tsitsiklis, Parallel and distributed computation : numerical methods. 1989.
Censor and Zenios, Parallel Optimization: Theory, Algorithms and Applications, 1997.

## Slide 15: Parallelization of Jacobi and Gauss-Seidel Iterations
Jacobi-type iteration
all components, simultaneously, updated with the current values and made available for next iteration
,
Synchronous update: next iteration waits until all updates are conducted
Gauss-Seidel Iteration
each update is computed with the latest available values of other components
,
The latest available may not be available, but earlier values, due to communication delay.
Asynchronous update: iterations starts as soon as any recent values are available.
Bertsekas and Tsitsiklis, Parallel and distributed computation : numerical methods. 1989.
Avron, et al, Revisiting asynchronous linear solvers: provable convergence rate through randomization, Journal of ACM, 2015.

## Slide 16: Stochastic gradient descent method
Instead of using full gradient, partial gradients of components are used.
Its sequential version is
Its asynchronous version is
, t.
Convex constraint leads extra projections onto convex sets.
Incremental gradient descent
Ordered-subset algorithm in engineering
Block-iterative method in image reconstruction
Kiwiel, Convergence of approximate and incremental subgradient methods for convex optimization, SIAM J. Optim., 2004.
Liu, et al, An Asynchronous Parallel Stochastic Coordinate Descent Algorithm, J. of Machine Learning Research, 2015.
Hannah and Yin, More Iterations per Second, Same Quality – why Asynchronous Algorithms may Drastically Outperform Traditional Ones, 2017. Preprint.

## Slide 17: Kaczmarz Algorithm
To solve systems of linear equations,
find (relaxed) projections onto each hyperplane iteratively,
It is an Gauss-Seidel iteration.
  Frank Natterer and Alfred Louis
Also called the algebraic reconstruction technique (ART)
, if

## Slide 18: Kaczmarz Algorithm
It is a stochastic gradient descent.
Its sequential version converges under the diminishing condition.
Its asynchronous iteration is not well covered in literature.

## Slide 19: Asynchronous Parallel Kaczmarz (I)
X3
X
X
X2
X1
Schedule/
Partition step
ART1
ART2
ART3
X3
X1
X2
Parallel Gauss-Seidel Iteration

## Slide 20: Asynchronous Parallel Kaczmarz (II)
Not the conventional Kaczmarz method.
More accelerators, more asynchronous updates with conflicts.
The hope is that later updates will resolve the conflicts, even slowly.
The solution is to use small or diminishing relaxations,
X1
X2
X3
A
C
B
X1 | A, C | t1 | A1, C1
X2 | A, B | t2 | A2, B2
X3 | C, B | t3 | C3, B3
In the next update of X1, will C1 or C3 be used?

## Slide 21: Experiments – Kaczmarz method(I)
No noise.
10 iteration
Display window not adjusted
Kaczmarz
Asynchronous parallel Kaczmarz with 3 threads

## Slide 22: Experiments – Kaczmarz method(IV)
Gaussian noise: 0.05
10 iteration
Display window = [0 1]
Kaczmarz
Asynchronous parallel Kaczmarz with 3 threads

## Slide 23: Heuristics for Asynchronous Parallelism
Heuristics
  欲速则不达：
  Haste does not bring success.
  Haste makes waste.
  Eile mit Weile. (from Google translate)
  Immer mit der Ruhe. (from Thomas Schuster)
Examples
  Lifting heavy object by a group people
  Painting a big picture by a group of painters
  My lessons
    Do not use full strength, but do it slowly and slowly.
    No waiting does not mean to be hash.
Expected performance
  reconstruction images in early iterations even with small or diminishing relaxation, as ordered-subset methods do.
Egyptian laborers lift the Stargate out of the ground in 1928
http://stargate.wikia.com/wiki/Tau'ri

## Slide 24: Convergence results (I)
Linear system of equations
[C. M.] symmetric and positive definite
  : convergence.
  : no convergence.
[L. W. S.] Consistent system under the same spectral condition.
Kaczmarz algorithm, or ART, does not fit.
Rosenfeld, A case study in programming for parallel-processors, Communications of the ACM, 1969. (research report in 1967).
Chazan and Miranker, Chaotic relaxation, Linear Algebra and its Applications, 1969.
Liu, Wright, and Sridhar, An Asynchronous Parallel Randomized Kaczmarz Algorithm, 2014. Preprint.

## Slide 25: Convergence results (II)
contraction.
Components update
  , ,
Extension of [C. M.]
Convergence for consistent linear systems
  weakly diagonal dominated matrices
  irreducible nonnegative matrix and positive solutions.
Kaczmarz does not fit.
Bertsekas and Tsitsiklis, Parallel and distributed computation : numerical methods. 1989.
Frommer, On asynchronous iterations, Journal of Computational and Applied Mathematics, 2000.
Frommer and Spiteri, On linear asynchronous iterations when the spectral radius of the modulus matrix is one. Topics in numerical analysis, 2001.

## Slide 26: One convergence result
Asynchronous version
.
Convexity
Diminishing relaxations
Bounded delay
  .
Nedić, Bertsekas, Borkar, Distributed asynchronous incremental subgradient methods, 2001.

## Slide 27: Diversified convergence results
Different asynchronous models
  Master or without master?
  Update all or partial solution vector?
Different combinations of object functions
  Fidelity + regularization
Different communication assumptions
  Mostly ambiguous
  Not well modelled w.r.t computing architecture.
Different relaxations
  Fixed or diminishing?
Deterministic or probabilistic convergence.
Low precision implementation
  Big data applications typically requires low accuracy
Liu, Wright, et al, An Asynchronous Parallel Stochastic Coordinate Descent Algorithm, J. of Machine Learning Research, 2015.
Hannah and Yin, More Iterations per Second, Same Quality – why Asynchronous Algorithms may Drastically Outperform Traditional Ones, 2017. Preprint.
De Sa, et al, Understanding and Optimizing Asynchronous Low-Precision Stochastic Gradient Descent, ISCA'17, 2017.

## Slide 28: CPU Operation vs Memory Access
x86 CPU fast for arithmetic operations
  ~1 cycle
X86 bus architecture slow for memory access
  ~10 cycle
Memory Wall
http://courses.cs.vt.edu/cs2506/Fall2014/Notes/L16.CachePoliciesAndPerformance.pdf
Intel® 64 and IA-32 Architectures
Optimization Reference Manual, 2016.
Writing Cache Friendly Code…
Memory protection from CPU instruction, to operating systems. …

## Slide 29: Asynchronous updates in data flow
CPU
System Cache
Main Memory
FPGA/GPU
Registers
On-board Memory
Complicated multiple asynchronous delays at arrow ends
, t.

## Slide 30: Outline
Background & Motivation
  Energy-efficient computing with FPGA
Asynchronous parallel iterative algorithms
  Communication model
FPGA implementation
  Techniques for implementation
Summary

## Slide 31: High-level Synthesis C->FPGA
Energy-efficient accelerator-rich architecture
Can be optimized under the performance, power, and cost constraints
Extensive use of accelerators (algorithmic blocks)
Limited onboard memory vs others
  Extendable
VivadoHLS of Xilinx
  https://www.xilinx.com/products/design-tools/vivado.html
How to design algorithms for FPGA?
  Asynchronous iterative parallel algorithms

## Slide 32: Beam-based SGD for Mumford-shah Regularization
Gamma-approximation by edge indicator
Beam-based gradient descent,
Alternative minimization algorithm for and
Enable fine-grained parallelism, natural for CT
Accelerators with minimum data communication
Reduce communication latency and back-projection computation
FPGA Acceleration for 3D Low-Dose Tomographic Reconstruction, submitted to IEEE Transactions on Parallel and Distributed Systems, 2019.
Notes: FPGA(4.8W)/CPU(95W):

## Slide 33: Implementation Techniques (I)
Pipeline for streaming dataflow
Achieve Load balance in the hardware pipeline.

## Slide 34: Tile-based memory optimization
Frequent large sized I/O of image and projection data in 3D.
  Memory intensive.
Tile the image and projection data
  Prefetching and buffering strategy.
  Mathematical problem has not formulated.
Achieve a high data reuse rate
Save the memory bandwidth
Increase performance
Linjun Qiao, Poster at this workshop.

## Slide 35: FPGA for XCT with Mumford-Shah

## Slide 36: Low-dose CT Experment
CT ACR 464 phantom on the
SOMATOM Definition AS at UCLA.
Voltage: 120KV
Current: 215, 150, 100, or 50mA.

## Slide 37: Results (SSIM)
8.5 minutes to reconstruct a typical 3D lung image with a quality comparable with the vendor’s result.

## Slide 38: Outline
Background & Motivation
  Energy-efficient computing with FPGA
Asynchronous parallel iterative algorithms
  Communication model
FPGA implementation
  Techniques for implementation
Summary

## Slide 39: Summary
Mumford-Shah regularization for XCT
  FPGA implementation with a quality comparable with the vendor’s result.
Asynchronous parallel computation is necessary for architectures with rich computing units
  multi-core CPU/GPU
  accelerators rich FPGA
  multi-node supercomputer
Algorithms with communication model
  Memory access/communication expense should not be ignored

## Slide 40
Supported by
  National Science Foundation of China (61520106004).
  National Basic Research and Development Program of China (973 Program) (2015CB351803).
Thank you for your attention.